## Slide 1: Tactile Keyboard using Micro-controller
Naman Kalkhuria (IEC2010065)
Prathak Rastogi (IEC2010093)
Prashant Mishra (IEC2010096)
A Mini-Project
Presentation on

## Slide 2: Abstract
In our project, we are implementing the technique of Voltage Drop Detection.
We are going to use Arduino Leonardo Board as Micro-controller board and we are going to use Processing programming language for programming the board.

## Slide 3: Motivation
Need of interaction
Most common type of interaction is touch.
To use day to day objects as keys of the keyboard.

## Slide 4: Scope
For detecting the touch on a door knob.
For making the objects act as key of the keyboard.
For making keyboard just by using the pencil and paper.
For use as a hidden keyboard so as to use as a security lock.

## Slide 5: Various Applications

## Slide 6: Introduction
Using Micro-controller for detecting the drop in the voltage when person touches the object.
One object act as one button and many objects can be used simultaneously.

## Slide 7: Touch of the object

## Slide 8: Circuit Diagram

## Slide 9: Block Diagram

## Slide 10: Sensing
Voltage Drop Detection.
Here, we monitor the change in voltage when the person touches the object.

## Slide 11: Various Operating Ranges:
ADC operating frequency = 200KHz
Update rate = 1Khz
Resistance value = 10MΩ to 22MΩ

## Slide 12: Various buttons we are trying to program using bananas as object:
Space bar
Arrow Keys
Some alphabets like Z, X, C, V, B, N, M.
We are programming less number of keys because of limited number of ADC channels available.

## Slide 13: Micro-controller Board
Arduino Leonardo

## Slide 14: Arduino Specs:
Microcontroller | ATmega32u4
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limits) | 6-20V
Digital I/O Pins | 20
PWM Channels | 7
Analog Input Channels | 12
DC Current per I/O Pin | 40 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 32 KB (ATmega32u4) of which 4 KB used by bootloader
SRAM | 2.5 KB (ATmega32u4)
EEPROM | 1 KB (ATmega32u4)
Clock Speed | 16 MHz

## Slide 15: Arduino IDE

## Slide 16: ATmega 32U4-Arduino Pin Mapping

## Slide 17: Processing Programming Language
Processing is for writing software to make images, animations, and interactions.
Processing includes a sketchbook, a minimal alternative to an integrated development environment (IDE) for organizing projects.

## Slide 18: Processing IDE

## Slide 19: THANK YOU